## Slide 1
YANG everywhere.
NETCONF for the core. CORECONF for the edge.
An 802.3 switch → 802.11 access point → client-device walkthrough
NETCONF • RFC 6241
RESTCONF • RFC 8040
CORECONF • RFC 9254/9595

## Slide 2
YANG models the data. NETCONF moves the data.
The data model is the contract; the protocol is the courier.
YANG
RFC 7950
• A modeling language for configuration & state
• Modules, containers, lists, leaves, types
• Constraints: ranges, patterns, must/when
• Operational vs config data (config false)
• Protocol-independent — one model, many wire formats
serialized & carried by
NETCONF
RFC 6241
• A protocol for configuring networks
• XML-encoded RPCs over SSH (RFC 6242)
• Datastores: running, candidate, startup
• Operations: get, edit-config, commit, …
• Reads/writes YANG-modeled data on a server
YANG was created so NETCONF (and later friends) had a formal, machine-readable model to encode and validate against.
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 3
Three protocols, one YANG model.
Same semantics — different wire format, different transport, different scale.
YANG — one data model (modules, containers, lists, leaves)
NETCONF
RFC 6241
Encoding
XML
Transport
SSH / TLS
Message
<rpc> / <edit-config>
Target
Routers, switches, big iron
Payload
Verbose, human-readable
RESTCONF
RFC 8040
Encoding
JSON or XML
Transport
HTTPS
Message
GET / POST / PUT / PATCH
Target
Web / cloud controllers
Payload
REST-friendly, moderate
CORECONF
RFC 9254 / 9595
Encoding
CBOR with numeric SIDs
Transport
CoAP (over UDP)
Message
GET / FETCH / iPATCH
Target
Constrained IoT devices
Payload
Tiny, binary
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 4
NETCONF protocol stack
Client ⟶ Server: XML RPCs over an SSH-secured session.
Client (mgmt station)
Content — YANG-modeled config/state
Operations — <get>, <edit-config>, <commit>
Messages — <rpc> / <rpc-reply> (XML)
Secure Transport — SSH (RFC 6242) / TLS
Server (switch / AP)
Content — YANG-modeled config/state
Operations — <get>, <edit-config>, <commit>
Messages — <rpc> / <rpc-reply> (XML)
Secure Transport — SSH (RFC 6242) / TLS
<edit-config> — XML over SSH
response
example wire payload — <edit-config> — XML over SSH
<rpc message-id="101" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config>
<target><running/></target>
<config>
<wifi-ap xmlns="urn:example:wifi-ap">
<latency>50</latency>
</wifi-ap>
</config>
</edit-config>
</rpc>
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 5
CORECONF protocol stack
Client ⟶ Server: CBOR-encoded YANG over CoAP — tiny, binary, numeric.
Client (AP / controller)
Content — YANG-modeled data (same model)
Operations — GET / FETCH / iPATCH
Encoding — CBOR map, keyed by SIDs
Transport — CoAP over UDP (optional OSCORE / DTLS)
Server (constrained device)
Content — YANG-modeled data (same model)
Operations — GET / FETCH / iPATCH
Encoding — CBOR map, keyed by SIDs
Transport — CoAP over UDP (optional OSCORE / DTLS)
iPATCH — CBOR/SID over CoAP
response
example wire payload — iPATCH — CBOR/SID over CoAP
POST coap://ap/c (code = 2.02 iPATCH)
Content-Format: 140 (application/yang-data+cbor; id=sid)
CBOR payload (annotated):
{ 70010: { # wifi-ap
70017: 50 # latency = 50 ms
} }
wire bytes: ~14 (vs. ~215 for the NETCONF XML above)
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 6
The example: switch → access point → device
Three YANG modules model the chain; NETCONF upstream, CORECONF to the edge.
Mgmt station
NETCONF
Switch (802.3)
NETCONF
Wi-Fi AP (802.11)
CORECONF
Device (client)
example-switch
container switch {
leaf name string;
leaf mgmt-address string;
leaf enabled boolean;
leaf ap-uplink-port uint8;
leaf uplink-up bool (ro);
leaf port-count uint8 (ro);
}
example-wifi-ap
container wifi-ap {
leaf name, ssid, band, channel;
leaf tx-power, latency, enabled;
leaf state (ro, identityref);
list device { // CORECONF-managed
key mac;
leaf hostname, ip-address,
signal-dbm, connected;
}
}
example-device
container device {
leaf mac string;
leaf hostname string;
leaf ip-address string;
leaf signal-dbm int8 (dBm);
leaf connected boolean;
}
// SID file assigns numeric SIDs
// used on the CORECONF hop
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 7
YANG snippet → instance data
Each module above becomes real data on the wire. Here are two of them.
example-switch.yang
module example-switch {
container switch {
leaf name { type string; }
leaf mgmt-address { type string; }
leaf enabled { type boolean; }
leaf ap-uplink-port { type uint8 { range "1..48"; } }
leaf uplink-up { type boolean; config false; }
leaf port-count { type uint8; config false; }
}
}
instance — NETCONF (XML)
// instance (NETCONF XML)
<switch xmlns="urn:example:switch">
<name>core-switch-1</name>
<mgmt-address>192.0.2.1</mgmt-address>
<enabled>true</enabled>
<ap-uplink-port>1</ap-uplink-port>
</switch>
example-wifi-ap.yang
container wifi-ap {
leaf name { type string; default "ap-1"; }
leaf enabled { type boolean; }
leaf ssid { type string; }
leaf channel { type uint8 { range "1..196"; } }
leaf tx-power { type uint8 { range "1..30"; } units "dBm"; }
leaf latency { type uint32 { range "0..10000"; } units "ms"; }
list device { key mac; /* ... */ }
}
instance — CORECONF (CBOR/SID)
// instance (CORECONF CBOR, SID-keyed, annotated)
{ 70010 (wifi-ap): {
70011 (name): "ap-1",
70012 (enabled): true,
70013 (ssid): "corp-wifi",
70015 (channel): 36,
70016 (tx-power): 20,
70017 (latency): 0
} }
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 8
A manager action cascades the chain
set-latency = 50 ms — three hops, two protocols, same YANG.
Mgmt station
Switch
Wi-Fi AP
Device
NETCONF <edit-config>
NETCONF <edit-config>
CORECONF iPATCH
hop 1 — station → switch (NETCONF)
<rpc message-id="101">
<edit-config>
<target><running/></target>
<config>
<wifi-ap xmlns="urn:example:wifi-ap">
<latency>50</latency>
</wifi-ap>
</config>
</edit-config>
</rpc>
~215 B payload
hop 2 — switch → AP (NETCONF)
// switch is a NETCONF
// client toward the AP
// — re-issues the same
// edit-config for the AP
<edit-config target running>
<wifi-ap xmlns=…>
<latency>50</latency>
</wifi-ap>
</edit-config>
~215 B payload
hop 3 — AP → (device scope) (CORECONF)
POST coap://ap/c
Code: 2.02 iPATCH
Content-Format: 140
CBOR payload:
{ 70010: { # wifi-ap
70017: 50 # latency
} }
~14 B payload
≈ 15× smaller than NETCONF
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 9
Why CORECONF for constrained devices?
Same YANG, right-sized protocol for the device at the edge of the chain.
set-latency = 50 ms (payload bytes)
NETCONF
~215 B
CORECONF
~14 B
≈ 15× smaller payload
Add CoAP/UDP vs SSH/TCP framing and the gap only widens.
Why it matters at the edge
• Battery life — fewer bytes = fewer radio-on-time milliseconds
• Memory — CBOR parser + CoAP stack fits in tens of KB
• Bandwidth — LPWAN / mesh / sub-GHz links are byte-counted
• Latency — no SSH handshake; CoAP works over UDP (and DTLS/OSCORE)
• SIDs — numeric identifiers remove string overhead entirely
• Same model — the device still speaks the same YANG as the controller
802-eth-dot11-mp • NETCONF ↔ CORECONF demo

## Slide 10
One standard, right-sized at each hop
IETF YANG + NETCONF/RESTCONF/CORECONF lets you keep one model from datacenter to sensor.
Mgmt station
NETCONF
Switch
NETCONF
Access point
CORECONF
Device
One YANG library
• Define the data model once (IETF or vendor YANG).
• Tooling (pyang, yanglint, confd, …) applies everywhere.
• No ‘edge-only’ or ‘cloud-only’ silo models to maintain.
Right protocol per link
• NETCONF where SSH + XML are already the ops lingua franca.
• RESTCONF where web/cloud controllers meet APIs.
• CORECONF where every byte and milliamp counts.
Open, interoperable, auditable
• All three are IETF standards — no vendor lock-in.
• The same validation rules on every hop.
• Easier security review — one model, one source of truth.
Model once in YANG. Transport right-sized per hop. Operate one chain end-to-end.
802-eth-dot11-mp • NETCONF ↔ CORECONF demo