## Slide 1
Modeling Once, Speaking Many
YANG with NETCONF, RESTCONF & CORECONF
One data model, three protocols — and why CORECONF wins on constrained links.
NETCONF · XML/SSH
RESTCONF · JSON/HTTP
CORECONF · CBOR/CoAP
Worked examples from the example-wifi-ap management chain.

## Slide 2
YANG and NETCONF: model vs. protocol
YANG defines WHAT the data is; NETCONF is HOW you move it.
YANG — the data modeling language (RFC 7950)
• Describes structure, types, constraints, and defaults.
• Hierarchy of containers, lists, leaves — vendor-neutral.
• One model serves every protocol below.
• Example: example-wifi-ap defines channel, latency, device{}.
NETCONF — the management protocol (RFC 6241)
• Operations get, edit-config, commit over a session.
• Datastores running / candidate / startup.
• Encoding XML, carried over SSH.
• Validates payloads against the YANG model.
YANG module
.yang
the single source
of truth
drives
NETCONF
XML / SSH
RESTCONF
JSON / HTTP
CORECONF
CBOR / CoAP
same model → three wire formats
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
2

## Slide 3
One family: NETCONF, RESTCONF, CORECONF
Same YANG models, different transports and encodings for different environments.
NETCONF
RFC 6241
Transport SSH / TCP
Encoding XML
Style session + datastores
Best for routers, data-center gear
Payload largest (verbose XML)
RESTCONF
RFC 8040
Transport HTTP / TLS
Encoding JSON or XML
Style RESTful CRUD on resources
Best for web / automation tooling
Payload medium (JSON)
CORECONF
draft-ietf-core-comi
Transport CoAP / UDP
Encoding CBOR + numeric SIDs
Style GET / FETCH / iPATCH
Best for constrained IoT devices
Payload smallest (binary + SIDs)
Shared foundation: the SAME YANG modules + the SAME datastore model (NMDA, RFC 8342)
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
3

## Slide 4
NETCONF: client → server message flow
Layered model (RFC 6241) — XML content over an SSH session.
Content
config / state data
Operations
<get>, <edit-config>, <commit>
Messages
<rpc>, <rpc-reply>, <notification>
Secure Transport
SSH (TCP/830)
💻
Client
manager
🗄
Server
device
<hello> capabilities
<rpc><edit-config>
<rpc-reply><ok/>
<rpc><get>
<rpc-reply><data>
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
4

## Slide 5
CORECONF: client → server message flow
Same YANG model, compact stack — CBOR + numeric SIDs over CoAP/UDP.
Content
CBOR map keyed by numeric SIDs
Methods
GET, FETCH, iPATCH on /c
Messaging
CoAP confirmable / Content-Format
Transport
UDP (5683) · optional OSCORE
📶
Client
AP (COMI)
📱
Server
device /c
GET /c
2.05 Content {CBOR}
iPATCH /c {70010:{70017:35}}
2.04 Changed
No session setup, no XML, datagram-friendly — SIDs replace long path strings.
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
5

## Slide 6
The wifi-ap model as a structure diagram
example-wifi-ap rendered PlantUML-style — a container owning a keyed device list.
« container » wifi-ap
+ name : string
+ enabled : boolean
+ ssid : string
+ band : wifi-band
+ channel : uint8 [1..196]
+ tx-power : uint8 dBm
+ latency : uint32 ms
~ state : identityref {ro}
« list » device
🔑 mac : string {key}
+ hostname : string
+ ip-address : string
+ signal-dbm : int8 dBm
+ connected : boolean
1 composition 0..*
key: mac
+ read-write (config) ~ read-only {ro} state 🔑 list key ◆—▶ composition (owns)
Same model the AP exposes over NETCONF upstream and CORECONF (SIDs) down to each device.
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
6

## Slide 7
Example: the wifi-ap YANG model
The single model the whole chain shares — example-wifi-ap@2026-10-05.
yang/example-wifi-ap@2026-10-05.yang
container wifi-ap {
leaf channel {
type uint8 { range "1..196"; }
default 36;
}
leaf latency {
type uint32 { range "0..10000"; }
units "milliseconds";
} // writable latency target
leaf state {
type identityref { base radio-state; }
config false; // read-only
}
list device { key "mac";
leaf mac { type string; }
leaf signal-dbm { type int8; }
leaf connected { type boolean; }
}
}
Why it matters
• Vendor-neutral contract for every node.
• Constraints (ranges, patterns) enforced on write.
• config false marks read-only operational state.
• One model — NETCONF upstream, CORECONF down.
example-wifi-ap@2026-10-05.sid
# .sid file assigns numeric SIDs
wifi-ap → 70010
channel → 70015
latency → 70017
state → 70018
device → 70020
mac → 70021
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
7

## Slide 8
Same instance data, three encodings
Set the AP latency target to 35 ms — identical semantics, very different byte counts.
NETCONF — edit-config (XML)
<rpc message-id="101"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config><target><running/></target>
<config>
<wifi-ap xmlns="urn:example:wifi-ap">
<latency>35</latency>
</wifi-ap></config>
</edit-config></rpc>
CORECONF — iPATCH (CBOR + SID)
iPATCH /c Content-Format: application/yang-instances+cbor-seq
CBOR (diagnostic): {70010: {70017: 35}}
│ └ latency value
└ wifi-ap > latency SID
CBOR (hex): A1 1A0001117A A1 1A00011181 1823
Payload size (real bytes)
NETCONF (XML)
215 B
CORECONF (CBOR/SID)
14 B
15.4×
smaller payload (215 B → 14 B)
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
8

## Slide 9
Processing "set latency = 35 ms" across the chain
A single manager action cascades down four nodes — NETCONF upstream, CORECONF to the device.
💻
Mgmt Station
NETCONF mgr
🔌
Switch
802.3
📶
Wi-Fi AP
coap:/c
📱
Device
CORECONF
NETCONF
edit-config · XML · 215 B
NETCONF
edit-config · XML · 215 B
CORECONF
iPATCH · CBOR/SID · 14 B
1 · Station
Manager issues edit-config setting wifi-ap/latency = 35 (XML over SSH).
2 · Switch
Validates against YANG, forwards the same edit-config to the AP (NETCONF).
3 · Access Point
Translates to CORECONF: iPATCH /c with {70010:{70017:35}} (CBOR/SID).
4 · Device
Applies the leaf, replies 2.04 Changed; ack propagates back up the chain.
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
9

## Slide 10
Why CORECONF for constrained applications
Built for the IoT edge: tiny payloads, no TCP, no XML parser.
📦 Tiny payloads
• CBOR + numeric SIDs replace verbose XML tag names.
• 15× smaller on the wire in this demo (215 B → 14 B).
• Fits a single UDP datagram — no fragmentation.
🔋 Low power & memory
• No TCP/TLS session state to maintain.
• No XML/JSON parser needed on the device.
• Less airtime → longer battery life on radios.
📡 Lossy-network friendly
• CoAP over UDP tolerates intermittent links.
• Confirmable messages give lightweight reliability.
• OSCORE (RFC 8613) secures without a TLS handshake.
🔁 Same model, no rework
• Reuse existing YANG modules unchanged.
• SIDs are a deterministic numeric mapping (RFC 9595).
• Tooling validates the same constraints end to end.
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
10

## Slide 11
Value of a hybrid YANG + NETCONF/CORECONF stack
Model once; choose the protocol that fits each hop.
One set of YANG models (RFC 7950 + NMDA, RFC 8342)
example-switch
example-wifi-ap
example-device
Core / managed network
NETCONF + RESTCONF
Rich transactions, candidate datastores,
mature tooling for switches & routers.
Constrained edge
CORECONF
CBOR/SID over CoAP for battery- and
bandwidth-limited IoT endpoints.
Takeaway: one data model, one skill set, one validation pipeline — open IETF standards, no vendor lock-in, and the right encoding on every hop.
YANG + NETCONF / RESTCONF / CORECONF · 802 management-chain demo
11

## Slide 12
Thanks — Questions?
One data model, the right protocol on every hop.
Scott Mansfield
✉ scott.mansfield@ericsson.com
NETCONF · XML/SSH
RESTCONF · JSON/HTTP
CORECONF · CBOR/CoAP